## Slide 1: Fourth Lab report Interference Optics PHOE-160
Spring 2021
Prof. Samuel Serna

## Slide 2: Groups
  Group A1:
  Group A2:
  Group B1:
  Group B2:

## Slide 3: Instructions
What is the material and what is the objective?
Safety first!
  Use plots
Finish the Lab report 1, 2 and 3
Polish the Lab Notebook, add pictures, explanations, etc
Keep working on your Company presentations
Some Elements:
  (Mounted) Source - CPS635R
  Mechanical mounts for the mirrors – KM100 and the Beam Splitter – could be RSP1D
  (2) Mirrors – ME1-G01
  Beam Splitter – EBS1
  Mechanical translation station – XR25 SERIES
  Post holders – PH2 and TR2
  Irises (if it is the case) or find a way to reference your height – ID20
  Height blockers – R2
  Powermeter – PM16-130

## Slide 4: Instructions
Some instructions:
Safety first! Goggles, signs, etc.
Use the mounted laser from last week CPS11K + CPS635R.
Use the mechanics : Post holders – PH2 and TR2 to mount 2 mirrors
Mount the ME1-G01 Mirrors
Use the height blocker R2
Use the LMR1 to mount the Beam Splitter EBS1
Mount the translation stage XR25 SERIES to the table
Mount one of the mirrors (correct the height) to the translation stage
Align the mirrors and the BS
Verify the effect of the location of one of the mirrors and its displacement
Follow the professor indications and ask if you have any doubt.
Describe ALL your procedures in your OneDrive Lab Notebook.
If there is time:
Adjust the proper post height for the irises ID20

## Slide 5: Table of Contents
Introduction
History
Famous Experiments
Measuring the Refractive Index of Air
Applications today!

## Slide 6: Introduction
The Michelson Interferometer is a superb instrument for measuring the optical properties of a medium.
E.g. refractive index, phase shifts, visualization of interference.

## Slide 7: History
https://www.aps.org/publications/apsnews/200711/physicshistory.cfm
By the late 1800s, physicists generally believed that light was a wave. Therefore, it was thought, it had to travel through some sort of medium, just as sound waves are vibrations in air. Scientists had believed for centuries that a mysterious, ghostly substance, known as the luminiferous ether, must permeate the universe and serve as a medium for the light waves. Various scientists attempted to detect the ether, with no success. Finally, in 1887 Albert Michelson and Edward Morley carried out their famous experiment, which provided strong evidence against the ether. They reported the results in November of that year, but both thought their experiment a failure and continued to cling to their belief in the ether.

## Slide 8: More history
Working in Berlin, he invented the device known as the Michelson interferometer. He realized he could use the setup to detect the Earth’s velocity through the ether. The basic design is simple and elegant. A beam of light is split and sent down two perpendicular paths. Then, after bouncing off mirrors, the two beams are recombined, producing an interference pattern. If the Earth was indeed traveling through the ether, the speed of light would differ depending on its direction with respect to the Earth’s motion through the ether, and Michelson’s interferometer would pick up a slight shift in the interference fringes. However, these early efforts found no evidence of the Earth’s movement with respect to the ether. Michelson was disappointed by the result and considered the experiment a failure.

## Slide 9: History
Introduced primarily in history to verify the existence of aether.
Special Relativity: might have influenced its development by Einstein.
Conclusion: regardless of its position (frame of ref.), the speed of light did not change.
Though disappointing to Michelson and Morley, the experiment revolutionized physics. Some scientists initially tried to explain the results while keeping the ether concept. For instance, George FitzGerald and Hendrik Lorentz independently proposed that moving objects contract along their direction of motion, making the speed of light appear the same for all observers. Then in 1905 Albert Einstein, with his groundbreaking theory of special relativity, abandoned the ether and explained the Michelson-Morley result, though it is uncertain whether Einstein was actually influenced by their experiment.
In 1889 Michelson moved to Clark University in Worcester, Massachusetts, and then in 1892 to the University of Chicago.

## Slide 10: Famous Experiment
The Michelson-Morley Experiment…the details!
Hypothesis: that there would be a phase shift, due to the aether, as the interferometer changed its orientation.
Conclusion: there was no change!!!

## Slide 11: Measuring the Refractive Index of Air
Set up
Process
  Calibration constant
Theory
  0.5* (1+2xi) where xi=1,2,3…
  * N= 2L*(natm-no)
  natm - 1 = DN× λv
  2L×(1 - r)

## Slide 12: Continued…
Results: natm - 1 = 2.7(8)e-4
Conclusion: Good!!!!

## Slide 13: Applications Today
One application of particular interest: the measurement of Gravitational Waves.
Used to study turbulence in wind-tunnels (the refractive index of air depends on its density), or the physical state of plasmas in fusion reactors.
https://phys.org/news/2019-05-ligo-virgo-neutron-star-smash-ups.html

## Slide 14: Additional Ressources
https://iwant2study.org/lookangejss/06QuantumPhysics/ejss_model_michelsoninterferometer/michelsoninterferometer_Simulation.xhtml
https://phet.colorado.edu/sims/html/wave-interference/latest/wave-interference_en.html
http://www.falstad.com/mathphysics.html
https://fr.slideshare.net/calvin_k/michelson-interferometer-46151946
https://www.lighttrans.com/applications/optical-metrology/interferometry.html

## Slide 15
https://www.youtube.com/watch?v=UA1qG7Fjc2A
https://www.youtube.com/watch?v=RRi4dv9KgCg