## Slide 1: Fifth Lab report Interference PHOE-160
Spring 2021
Prof. Samuel Serna

## Slide 2: Groups
  Group A1:
  Group A2:
  Group B1:
  Group B2:

## Slide 3: Instructions
What is the material and what is the objective?
Safety first!
  Use plots
Finish the Lab report 1, 2 and 3
Polish the Lab Notebook, add pictures, explanations, etc
Keep working on your Company presentations
Some Elements:
  (Mounted) Source - CPS635R
  Mechanical mounts for the mirrors – KM100 and the Beam Splitter – could be RSP1D
  (2) Mirrors – ME1-G01
  Beam Splitter – EBS1
  Mechanical translation station – XR25 SERIES
  Post holders – PH2 and TR2
  Irises (if it is the case) or find a way to reference your height – ID20
  Height blockers – R2
  Powermeter – PM16-130

## Slide 4: Instructions
Some instructions:
Safety first! Goggles, signs, etc.
Use the mounted laser from last week CPS11K + CPS635R.
Use the mechanics : Post holders – PH2 and TR2 to mount 2 mirrors
Mount the ME1-G01 Mirrors
Use the height blocker R2
Use the LMR1 to mount the Beam Splitter EBS1
Mount the translation stage XR25 SERIES to the table
Mount one of the mirrors (correct the height) to the translation stage
Align the mirrors and the BS
Verify the effect of the location of one of the mirrors and its displacement
Follow the professor indications and ask if you have any doubt.
Describe ALL your procedures in your OneDrive Lab Notebook.
If there is time:
Adjust the proper post height for the irises ID20

## Slide 5: Procedure
Use the mounts and the beam splitter to separate the beam in two different paths as shown in the figure. Describe ALL your procedures in your OneDrive Lab Notebook.
Wear Gloves!

## Slide 6: Set-up
Add the mirrors to send the beam back via reflection. Locate one of the mirror (in one arm) on the mechanical stage to change the optical path length precisely.

## Slide 7: Procedure
Take images with the silicon camera (or with your phone)
Describe what happens when the mirror in one of the arms gets displaced.
By how much did you need to displace it to see any noticeable different?

## Slide 8: Additional Ressources
https://iwant2study.org/lookangejss/06QuantumPhysics/ejss_model_michelsoninterferometer/michelsoninterferometer_Simulation.xhtml
https://phet.colorado.edu/sims/html/wave-interference/latest/wave-interference_en.html
http://www.falstad.com/mathphysics.html
https://fr.slideshare.net/calvin_k/michelson-interferometer-46151946
https://www.lighttrans.com/applications/optical-metrology/interferometry.html

## Slide 9
https://www.youtube.com/watch?v=UA1qG7Fjc2A
https://www.youtube.com/watch?v=RRi4dv9KgCg