## Slide 1: Third Lab report Polarization Optics PHOE-160
Spring 2021
Prof. Samuel Serna

## Slide 2: Groups
  Group A1:
  Group A2:
  Group B1:
  Group B2:

## Slide 3: Instructions
What is the material and what is the objective?
Safety first!
  Use plots
Finish the Lab report 1, 2 and 3
Polish the Lab Notebook, add pictures, explanations, etc
Keep working on your Company presentations
Some Elements:
  (Mounted) Source - CPS635R
  Mechanical mounts for the polarizers – RSP1D
  Polarizers – LPVISE100-A
  Post holders – PH2 and TR2
  Irises (if it is the case) or find a way to reference your height – ID20
  Height blockers – R2
  Powermeter – PM16-130

## Slide 4: Instructions
Some instructions:
Safety first! Goggles, signs, etc.
Use the mounted laser from last week CPS11K + CPS635R.
Use the mechanics : Post holders – PH2 and TR2 to mount a LPVISE100-A
Mount the linear polarizer RSP1D
Use the height blocker R2
Use the screen EDU-VS1 to constantly block the light.
Use the powermeter software in your PC and use the device: PM16-130
Measure the power before and after the polarizer, take different measurements by rotating the polarizer.
Repeat the procedures to mount a second identical polarizer.
Adjust the proper post height for the irises ID20
Fix the angle for the maximum transmission of both polarizer.do not touch any more the angle of the polarizer closest to the laser.
Take measurements every 10 degrees. Until reaching 360 degrees, so 36 measurements in total.
Demonstrate Malus Law.
Follow the professor indications and ask if you have any doubt.
Describe ALL your procedures in your OneDrive Lab Notebook.

## Slide 5: Polarization
Polarization refers to the direction of oscillation of the electric field in an electromagnetic wave.
It could be linear, circular, elliptical and more generally, random.
https://www.physicsclassroom.com/class/light/Lesson-1/Polarization

## Slide 6: 1. Two Polaroid Sheets
If you pass light through two Polaroid sheets so that their polarization axes are aligned, light will be transmitted through both of them.
If their axes are at right angles to each other, almost no light will get through. When Polaroids are used in pairs like this, the first is called the polarizer and the second is called the analyzer.
http://hyperphysics.phy-astr.gsu.edu/hbase/phyopt/polcross.html

## Slide 7: 2. Polarization by reflection
When an unpolarized light wave reflects off a non-metallic surface, it can be completely polarized, partially polarized or unpolarized depending on the angle of incidence. A completely polarized wave occurs for an angle called Brewster’s angle (named after Sir David Brewster)
http://hyperphysics.phy-astr.gsu.edu/hbase/phyopt/polref.html

## Slide 8: 2. Polarization by reflection
Different polarization of light get reflected and refracted with different amplitudes (“birefringence”).
At one particular angle, the parallel polarization is NOT reflected at all!
This is the “Brewster angle” qB, and qB+ qr=90o.

## Slide 9: Applications
Knowing that reflected light or glare from surfaces is at least partially plane polarized, one can use Polaroid sunglasses. The polarization axes of the lenses are vertical as the glare usually comes from reflection off horizontal surfaces.
https://www.polaroideyewear.com/

## Slide 10: 3. Polarization by scattering
When light(such as that from the sun) shines on particles, they can absorb and then reradiate part of the light. The absorption and reradiation of light is called scattering. Unpolarized light will be partially plane polarized after scattering from small particles of dust etc…The scattered light will be completely plane polarized if scattered light is 90.0o from incident light. Thus if you look straight up into the sky and rotate a polarizer, you will see the transmitted light change in intensity. (Blue light is scattered more than red light so the sky appears blue!!)
https://sciencedemonstrations.fas.harvard.edu/presentations/polarization-scattering

## Slide 11: Optical Activity
A substance is said to be optically active if it can rotate the plane of polarization of transmitted light. The angle through which the light is rotated depends on the length of the sample and the concentration if the substance is in solution. A standard method for measuring the concentration of a sugar solution is to measure the rotation produced by a fixed length.
https://www.chem.ucalgary.ca/courses/350/Carey5th/Ch07/ch7-4.html

## Slide 12: Stress and polarization
Some materials are optically active because of the shape of the molecules. Other materials such as glass or plastic become optically active when placed under stress. Engineers build plastic models of various structures such as machine parts. The model is analyzed under different load conditions. Polarized light is passed through the plastic and then through an analyzer whose axis is perpendicular to the polarized light. Regions of greatest stress produce the greatest angles of rotation so these show up as bright bands.
https://www.exploratorium.edu/snacks/bone-stress#:~:text=Polarized%20light%20reveals%20stress%20patterns,illustrate%20stresses%20found%20in%20bones

## Slide 13: Additional Ressources
https://www.uv.es/indoptic/applets/Malus/index.html
https://www.olympus-lifescience.com/en/microscope-resource/primer/java/polarizedlight/3dpolarized/
https://iwant2study.org/lookangejss/04waves_13light/ejss_model_polarizer/polarizer_Simulation.xhtml
https://www.physicsclassroom.com/class/light/Lesson-1/Polarization