## Slide 1: Lecture 2 Reflection and refraction PHOE-160
Spring 2021
Prof. Samuel Serna

## Slide 2: Groups
  Group A1:
  Group A2:
  Group B1:
  Group B2:

## Slide 3: Instructions
What is the material and what is the objective?
Safety first!
  Use plots
Finish the Lab report 1
Polish the Lab Notebook, add pictures, explanations, etc
Keep working on your Company presentations
Some Elements:
  (Mounted) Source - CPS635R
  Mechanical mounts for the lenses – LMR1
  Post holders – PH2 and TR2
  Irises (if it is the case) or find a way to reference your height – ID20
  Height blockers – R2
  Powermeter – PM16-130

## Slide 4: Instructions
Safety first! Goggles, signs, etc.
Use the mounted laser from last week CPS11K + CPS635R.
Use the mechanics : Post holders – PH2 and TR2 to mount a LMR1
Mount the LA1131-A-ML, note the focal length
Learn how to use the height blocker R2
Use the screen EDU-VS1 to constantly block the light and then to find the focal point.
Mount (PH2+TR2+BA2) and use the powermeter software in your PC and use the device: PM16-130
Measure the power before and after the lens, annotate your observations.
Repeat the procedures to mount LA1608-A-ML, note the focal length.
Use a BA2 to locate the second lens at its focal distance from the focal point you just measured.
Find the collimated beam (what is collimation?)
Adjust the proper post height for the irises ID20
Follow the professor indications and ask if you have any doubt.
Describe ALL your procedures in your OneDrive Lab Notebook.

## Slide 5: Some material
Laser source (Gain medium, pump and cavity):
Device : CPS635R RED LIGHT (635 nm)
Safety sign, specify:
The laser class
The required optical density (OD)
The wavelength (in nm)
Safety goggles LG4
Mounted mirrors

## Slide 6: What happens to light after impacting a reflective surface?
Law of reflection: the angle of reflection (that the ray makes with the normal to a surface) equals the angle of incidence.
Normal to the surface
= Angle of incidence
= Angle of reflection
Please pay attention to the units of the angle and your calculator/computer configuration
=

## Slide 7: Diffuse reflection
When the surface is not totally flat, the law of reflection still holds but the angle of incidence varies.
Reflection law still holds locally

## Slide 8: Refraction: Snell’s Law
Refraction is what makes objects half-submerged in water look odd.
Normal to the surface
= Angle of incidence
= Angle of reflection
=
are the refractive indices of the upper and the lower medium, respectively.

## Slide 9: Problem to be done in class 1
A ray coming from air into a glass piece.
What are the refractive indices in the red?
  https://refractiveindex.info/
  https://refractiveindex.info/?shelf=main&book=SiO2&page=Malitson
  https://refractiveindex.info/?shelf=other&book=air&page=Ciddor
  If , what is
  https://www.wolframalpha.com/
Notes: Approx 29 degrees

## Slide 10: Problem to be done in class 2
What is the angle ?
Refractive index database: https://refractiveindex.info/
Glass:
Air
Air

## Slide 11: Resources
https://www.olympus-lifescience.com/fr/microscope-resource/primer/lightandcolor/reflectionintro/
https://www.youtube.com/watch?v=oMnIJEqSRVs
https://www.edmundoptics.fr/knowledge-center/video/tutorials/understanding-refraction/
https://phet.colorado.edu/en/simulations/bending-light