## Slide 1: Third Lab report Polarization PHOE-160
Spring 2021
Prof. Samuel Serna

## Slide 2: Groups
  Group A1:
  Group A2:
  Group B1:
  Group B2:

## Slide 3: Instructions
What is the material and what is the objective?
Safety first!
  Use plots
Finish the Lab report 1, 2 and 3
Polish the Lab Notebook, add pictures, explanations, etc
Keep working on your Company presentations
Some Elements:
  (Mounted) Source - CPS635R
  Mechanical mounts for the polarizers – RSP1D
  Polarizers – LPVISE100-A
  Post holders – PH2 and TR2
  Irises (if it is the case) or find a way to reference your height – ID20
  Height blockers – R2
  Powermeter – PM16-130

## Slide 4: Instructions
Some instructions:
Safety first! Goggles, signs, etc.
Use the mounted laser from last week CPS11K + CPS635R.
Use the mechanics : Post holders – PH2 and TR2 to mount a LPVISE100-A
Mount the linear polarizer RSP1D
Use the height blocker R2
Use the screen EDU-VS1 to constantly block the light.
Use the powermeter software in your PC and use the device: PM16-130
Measure the power before and after the polarizer, take different measurements by rotating the polarizer.
Repeat the procedures to mount a second identical polarizer.
Adjust the proper post height for the irises ID20
Fix the angle for the maximum transmission of both polarizer.do not touch any more the angle of the polarizer closest to the laser.
Take measurements every 10 degrees. Until reaching 360 degrees, so 36 measurements in total.
Demonstrate Malus Law.
Follow the professor indications and ask if you have any doubt.
Describe ALL your procedures in your OneDrive Lab Notebook.

## Slide 5: Procedure
Use the mounts and the polarizers to measure the power at different distances in the optical axis. Describe ALL your procedures in your OneDrive Lab Notebook.
Wear Gloves!

## Slide 6: Set-up

## Slide 7: Procedure
We will verify Malus' Law, which predicts a cosine squared dependency of the intensity as a function of the angle between the polarizer and the analyzer (or the two polarizers).
Fix the first polarizer and allow the rotation of the second one.
Take one measure of the power every 10 degrees of rotation.
Complete the 37 measurements to finish the circle and arrive back to the first measurement point.
Plot the values and compare it with a cosine squared.

## Slide 8: Additional Ressources
https://www.uv.es/indoptic/applets/Malus/index.html
https://www.olympus-lifescience.com/en/microscope-resource/primer/java/polarizedlight/3dpolarized/
https://iwant2study.org/lookangejss/04waves_13light/ejss_model_polarizer/polarizer_Simulation.xhtml
https://www.physicsclassroom.com/class/light/Lesson-1/Polarization