## Slide 1: Fundamentals of Laser
1

## Slide 2: Layout
2
Introduction
Properties of Laser Light
Basic Components of Laser
Basic laser operation
Three Level Laser System
Types of Lasers
Optical Sources & Photodetectors

## Slide 3: Introduction
3
LASER
Light Amplification by Stimulated Emission of Radiation.
An optical source that emits photons in a coherent beam.
In analogy with optical lasers, a device which produces any particles or electromagnetic radiations in a coherent state is called “Laser”, e.g., Atom Laser.
In most cases “laser” refers to a source of coherent photons i.e., light or other electromagnetic radiations. It is not limited to photons in the visible spectrum. There are x-ray lasers, infrared lasers, infrared lasers etc.

## Slide 4: Properties of Laser Light
4
The light emitted from a laser is monochromatic, that is, it is of one color/wavelength. In contrast, ordinary white light is a combination of many colors (or wavelengths) of light.
Lasers emit light that is highly directional, that is, laser light is emitted as a relatively narrow beam in a specific direction. Ordinary light, such as from a light bulb, is emitted in many directions away from the source.
The light from a laser is said to be coherent, which means that the wavelengths of the laser light are in phase in space and time. Ordinary light can be a mixture of many wavelengths.

## Slide 5: Ordinary Light vs. Laser Light
Ordinary Light
Laser Light
5

## Slide 6: Basic Components of Laser
1
Laser system consists of three important parts.
Active medium or laser medium
An energy source (referred to as the pump or pump source)
An optical resonator consisting of a mirror or system of mirrors
6

## Slide 7: Basic Components of Laser 2
7
Active Medium
The active medium is the major determining factor of the wavelength of operation, and other properties, of the laser. There are hundreds of different gain media in which laser operation has been achieved. The gain medium is excited by the pump source to produce a population inversion, and it is in the gain medium that spontaneous and stimulated emission of photons take place leading to the phenomenon of optical gain or amplification. The gain medium may be solid crystals such as ruby or Nd:YAG, liquid dyes, gases like CO2 or Helium/Neon, or semiconductors such as GaAs.
Pumping Mechanism
The pump source is the part that provides energy to the laser system. Examples of pump sources include electrical discharges, flash lamps, arc lamps, light from another laser, chemical reactions and even explosive devices. The type of pump source used principally depends on the gain medium.
Optical Resonator
The optical resonator or optical cavity, in its simplest form is two parallel mirrors placed around the gain medium which provide feed back of the light. Light from the medium produced by the spontaneous emission is reflected by the mirrors back into the medium where it may be amplified by stimulated emission. One of the mirrors reflects essentially 100% of the laser light while the other reflects less than 100% of the laser light and transmits the remainder.

## Slide 8: Basic Principles of Light Emission and Absorption 1
In 1916, Einstein considered various transition rates between atomic states (say, 1 and 2) involving light of intensity, I.
Absorption:
Absorption is the process by which the energy of the photon is taken up by another entity, e.g., by an atom whose valence electrons make transition between two electronic energy levels. The photon is destroyed in the process.
Rate of Stimulated Absorption =B N1 I
B Einstein's Coefficient for Stimulated Absorption
N1 Population in the Ground State
8

## Slide 9: Basic Principles of Light Emission and Absorption 2
Stimulated Emission:
  process by which, when perturbed by a photon, matter may lose energy resulting in the creation of another identical photon.
Rate of stimulated emission = B N2 I
  Einstein's Coefficient for Stimulated Emission
N2 Population in the Excited State
Spontaneous Emission:
A process by which an atom, molecule in an excited state drops to a lower energy level.
Rate of spontaneous emission = A N2
A Einstein’s Coefficient for Spontaneous Emission
9

## Slide 10: Threshold Condition
R = 100%
R < 100%
I0
I1
I2
I3
Laser medium
10
with gain, G
A laser action will be achieved if the beam increases in intensity during a round trip: that is, if I3 t I0
Usually, additional losses in intensity occur, such as absorption, scat- tering, and reflections. In general, the laser will lase if, in a round trip:
Gain > Loss This is called achieving Threshold.

## Slide 11: Laser Gain
Neglecting spontaneous emission:
dI dI
dt dz
G { exp^V >N2 - N1 @ L`
g { >N2 - N1 @V D { >N1 - N2 @V
If N2 > N1:
If N2 < N1 :
I (z) I (0) exp^V >N2 - N1 @ z`
There can be exponential gain or loss in intensity.
Normally, N2 < N1, and there is loss (absorption).
But if N2 > N1,
there’s gain, and we define the gain, G:
Laser medium
I(0)
0 L
I(L)
z
Proportionality constant is the absorption/gain cross- section, V
11
c v BN2 I - BN1I
v B >N2 - N1 @ I
[Stimulated emission minus absorption]

## Slide 12: Population Inversion
12
In order to achieve G > 1, that is, stimulated emission must exceed absorption:
B N2 I > B N1 I
Equivalently,
This condition is called population inversion. It does not occur naturally. It is inherently a non-equilibrium state.
In order to achieve inversion, we must pump the laser medium in some way and choose our medium correctly.
Population inversion is the necessary condition for laser action.
N2 > N1

## Slide 13: Two-, Three-, and Four-Level Systems
Two-level system
Laser Transition
Pump Transition
At best, you get equal populations.
No lasing.
Three-level system
If you hit it hard, you get lasing.
Four-level system
Lasing is easy!
Laser Transition
Fast decay
13
Fast decay
Fast decPauymp
Transition

## Slide 14: Three Level Laser System 1
14
•
•
•
•
•
•
Energy is applied to a medium raising electrons to an unstable energy level.
These atoms spontaneously decay to a relatively long-lived, lower energy, metastable state.
A population inversion is achieved when the majority of atoms have reached this metastable state.
Lasing action occurs when an electron spontaneously returns to its ground state and produces a photon.
If the energy from this photon is of the precise wavelength, it will stimulate the production of another photon of the same wavelength and resulting in a cascading effect.
The highly reflective mirror and partially reflective mirror continue the reaction by directing photons back through the medium along the long axis of the laser.
The partially reflective mirror allows the transmission of a small amount of coherent radiation that we observe as the “beam”.
Laser radiation will continue as long as energy is applied to the lasing medium.

## Slide 15: Three Level Laser System
Energy
Introduction
Ground State
Excited State
Metastable State
Stimulated Emission of Radiation
Spontaneous Energy Emission
15
2

## Slide 16
2
3
4
Lasing Medium at Ground State
Pump Energy (Electrical, Optical, Chemical, etc )
,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j, ,j,
• • • • • •
• • • •
• •
• A • •
•
V •
•
• • V .
•
••••••••••
• • • • • • A • •
0 • •• • • • •
A • • • • •
• •
• • •
V. •
•
• • • •
A
• • • • • •• V• • • •
•• • • 0 • •• • ••
• •• • ••
Population Inversion
Spontaneous Emission, Start of Stimulated Emission
0
Ground State
•
Energy Level 1
•
Energy Level 2
•
Spontaneous Emission
0
Stimulated Emission
The o are atoms, ions, or molecules depending on lasing medium.
Stimulated Emission Building Up
Laser Beam
5
Full Stimulated Emission, Coherent Laser Beam Generated
Basic Laser Operation

## Slide 17: Laser Beam Properties
Many lasers operating on fundamental Transverse mode, or TEM00 mode of the laser resonator, emit beams with a Gaussian profile.
For a Gaussian beam, the complex electric field amplitude, measured in volts per meter, at a distance r from its centre, and a distance z from its waist, is given by
where w(z) Beam width or spot size
R(z) Radius of Curvature
ȗ(z) Longitudinal Phase delay
If beam is not a pure Gaussian shape, the transfer modes of the beam may be analyzed as a superposition of Hermite-Gaussian or
Laguerre-Gaussian beams.

## Slide 18: Laser Output
The output of a laser may be continuous having constant amplitude known as continuous wave or it may be pulsed, which is achieved by using the techniques of Q-switching and Mode locking
Energy
(Watts)
Time
Continuous Output (CW)
Pulsed Output (P)
Energy
(Joules)
Time
watt (W) - Unit of power or radiant flux (1 watt = 1 joule per second).
Joule (J) - A unit of energy
Energy (Q) The capacity for doing work. Energy content is commonly used to characterize the output from pulsed lasers and is generally expressed in Joules (J).
Irradiance (E) - Power per unit area, expressed in watts per square centimeter.

## Slide 19: Types of Lasers
Solid-state lasers have lasing material distributed in a solid matrix (such as ruby or neodymium:yttrium-aluminum garnet "YAG"). Flash lamps are the most common power source. The Nd:YAG laser emits infrared light at 1.064 nm.
Semiconductor lasers sometimes called diode lasers, are pn junctions. Current is the pump source. Applications: laser printers or CD players.
Dye lasers use complex organic dyes, such as rhodamine 6G, in liquid solution or suspension as lasing media. They are tunable over a broad range of wavelengths.
Gas lasers are pumped by current. Helium-Neon lases in the visible and IR. Argon lases in the visible and UV. CO2 lasers emit light in the far-infrared (10.6 mm), and are used for cutting hard materials.

## Slide 20: Optical Sources & Photodetectors

## Slide 21: Optical Sources 1
•
•
•
Several important factors enter into selecting an optical source for Fibre-optic system.
The light must be at a wavelength transmitted effectively by the optical fibre, usually the 850, 1300, or 1550 nm for glass fibre (silica) and around 660 nm in plastic fibre.
The range of wavelength is also important, because larger the range, the larger the potential for dispersion problems.
The light source must generate adequate power to send the signal through the fibre, but not so much power that it causes non- linear effects or distortion in the fibre or receiver.
The light source must transfer it’s output effectively into the fibre.

## Slide 22: Optical Sources
2
The main optical sources used with fibre-optic systems are semiconductor devices:
Light- Emitting Diode
Diode laser
Fibre laser
WHAT IS A DIODE?

## Slide 23: Diode
1
semiconductor device, consists of N-
A diode is the simplest sort of
type and P-type semiconductor, having electrodes on each end.
This arrangement conducts electricity in one direction only
At the junction, free electrons from the N-type material fill holes from the P-type material. This creates an insulating layer in the middle of the diode called the depletion zone.

## Slide 24
Diode 2
When the negative end of the circuit is hooked up to the N-type layer and the positive end is hooked up to P-type layer, electrons and holes start moving and the depletion zone disappears

## Slide 25: Diode 3
When the positive end of the circuit is hooked up to the N-type layer and the negative end is hooked up to the P-type layer, free electrons collect on one end of the diode and holes collect on the other. The depletion zone gets bigger.

## Slide 26: Light Emitting Diode
A light emitting diode is a forward biased semiconductor diode in which recombination at the junction produces light.
Light emitting diodes are not lasers. They produce light spontaneously, in every direction like light bulbs.

## Slide 27: Working Principle of LEDs
A small voltage is applied across a semiconductor diode, causing a current to flow across the junction.
When an electron drops from the conduction level to valence level it releases the difference in energies between the two levels in the form of photons.
The band-gap difference between the energy levels and hence the amount of energy released and the emitted wavelength-depends on the composition of the semiconductor.
In many semiconductors, notably silicon and germanium, the released energy is dissipated as heat- vibration of the crystalline lattice. In order to have a photonic emission, combination of semiconductors materials are used.

## Slide 28: Working materials for LEDs
Semiconductor Compunds | Operating Wavelength
GaAs | 930 nm
GaAlAs | 750 -900 nm
GaAsP | 665 nm
InGaAsP | 1300 -1550 nm
The usual LEDs used in fibre optic systems are made of Gallium-Aluminium-Arsenide or Gallium-Arsenide compounds.
The most important compound for high performance optical fibre optics is InGaAsP

## Slide 29: Advantages & Disadvantages of LEDs
Produce more light per Watt than do incandescent bulbs.
Can emit light of an intended color without the use of color filters that traditional lighting methods require..
The solid package of an LED can be designed to focus its light.
Are built inside solid cases that protect them, making them extremely durable.
Light up very quickly.
Can be very small and are easily populated onto printed circuit boards.
Are currently more expensive, than more conventional lighting technologies .
Require complex power supply setups to be efficiently driven.

## Slide 30: Applications of LEDs
Status indicators on all sorts of equipment
Traffic lights and signals
Exit signs
Toys and recreational sporting goods, such as the Flashlight
Light bars on emergency vehicles.
Elevator Push Button Lighting
Thin, lightweight message displays at airports and railway stations and as destination displays for trains, buses, trams and ferries.
Remote controls, such as for TVs and VCRs, often use infrared LEDs.
In optical fiber and Free Space Optics communications.
In dot matrix arrangements for displaying messages.
Glow lights, as a more expensive but longer lasting and reusable alternative to Glow sticks.
Movement sensors, for example in optical computer mice.

## Slide 31: Diode Laser
A diode Laser ( or semiconductor laser) is superficially like LEDs.
•
•
Both devices generate light from recombination of electron-hole pairs.
In both light output is proportional to the drive current.
The output wavelength depends on the material’s band gap.
•
There are two important functional differences between LEDs and Diode lasers.
The diode laser needs much higher current to produce a large concentration of electron-hole pairs, to dominate stimulated emission on absorption.
The current must be high to maintain population inversion, at the junction.
In laser diode positive feedback for stimulated emission is obtained from smooth “facets” formed by cleaving the semiconductor crystal at junction planes.

## Slide 32: Structure of Diode Laser
A diode laser must contain at least three layers- a p-type, a n-type and a separate active layer ( either n or p-type) which emits the light.
A high-performance diode lasers usually contain more layers.
The boundaries between the active layer and the surrounding layers are very important in determining efficiency of a diode laser.
Layers of different materials help confining light more efficiently in the active layer.

## Slide 33: Homostructure and Heterostructure diode lasers
Diode lasers, with all layers made of same material are called homostructure or homojunction lasers.
Diode lasers, in which adjacent layers are made of different materials are called heterostructure or heterojunction lasers.
In double heterostructure laser has higher refractive index than either of the two adjacent layers, this helps confine light

## Slide 34: Operating Wavelengths
The
wavelengths of diode
laser depends on composition of the junction layers, like
those of LEDs.
The primary composition used in diode laser light source for
fiber optics are variations on the standard III-V
semiconductor
compounds that can be fabricated on
substrates of Ga-As or In-P.
Ga(1-x)AlxAs on GaAs for 780-850 nm In0.73Ga0.27As0.58P0.42 on InP for 1310 nm
In0.58Ga0.42As0.9P0.1 on InP for1550 nm

## Slide 35: Output Spectrum
Diode laser have much narrower spectral width than LEDs, allowing the use of diode lasers to carry high-speed signals through fibre with low dispersion at the laser wavelength.
The line-width of 1 to 3 nm is large enough to cause dispersion in single- mode fibre.
The wavelengths that are amplified are those for which the round-trip distance between the mirrors is an integral number of wavelengths.
2D =NO
where 2D is the round trip distance and N is an integer.

## Slide 36: Fibre Lasers
All lasers work by amplifying stimulated emission, but they do so in different ways.
One family consists of glasses or crystals doped with small quantities of elements that can be excited by light from an external source, then stimulated to emit light at a longer wavelength.
If laser material is made in the form of a fibre, with core doped with the light –amplifying impurity, this doped fibre can serve as a laser (putting mirrors on both ends) or as an amplifier.
One example is an Erbium-fibre laser

## Slide 37: Basic operation of fibre laser
Light from an external diode laser emitting at 980 or 1480 nm excites erbium atoms in the fibre.
When a weak signal at 1550 nm enters the fibre, those light waves can stimulate the erbium atoms to release their stored energy as additional 1550 nm light waves.
The process continues as the signal passes through the fibre, building a stronger and stronger signal (Amplifier).
Putting mirrors on both ends of an erbium-doped fibre makes a fibre laser.

## Slide 38: Detectors
Detectors
A device used for detection, most commonly for electromagnetic waves.
There is a wide variety of detectors used from radio waves to x- rays and Ȗ-rays.
Basic requirements for detectors in Fibre optics
High sensitivity (must match with source wavelength)
Wide bandwidth (high speed response)
Small/low noise factor
Immune to environment
Modes power requirements (can work with low power sources with nominal power consumption)

## Slide 39: Materials for Photodetectors
Most
1.
2.
3.
There
commonly used material for photodetectors are
Silicon
Gallium Arsenide (GaAs)
Germanium Indium Phosphide ( GInP).
wavelengths response depends on their composition
Materials | Operating Wavelength
Silicon | 400-1000 nm
Germanium | 600-1600 nm
GaAs | 800-1000 nm
InGaAs | 1000- 1700 nm
InGAsP | 1100-1600 (doping dependent)

## Slide 40: Photodetector
Optical detectors / Photodectectors Solar Cells:
The simplest semiconductor detector are solar cells.
Incident light energy raises valence band electron to the conduction band, generating an electric voltage
Such photovoltaic detectors are slow and not very sensitive.
Photodiodes:
Semiconductor devices for the detection of light. They contain a p-n junction

## Slide 41: Photodiodes
1
Photodiodes operate in two modes
Photovoltaic Mode: Like Solar cell, illuminated photodiode generates a current at zero bias.
Photoconductive Mode: A reverse voltage is applied to photodiode and resulting photocurrents is measured.
Photodiode are faster, more sensitive if electrically reversed biased.
The reversed-bias draws current-carrying electrons and holes out of the junction region, creating a depleted region, which stops the current flow.
A photon of suitable wavelength can create electron-hole pairs in this region by raising an electron from the valence band to the conduction band, leaving behind a hole.
The bias voltage causes these current carriers to drift quickly away from junction region. So current flows proportional to the photon on the detector.

## Slide 42: Features of Photodiode
Critical performance parameters of a photodiode include:
Responsitivity
The ratio of generated photocurrent to incident light power, typically expressed in A/W when used in photoconductive mode.
Dark Current
The current through the photodiode in the absence of any input optical signal, when it is operated in photoconductive mode.
Noise-Equivalent Power
The minimum input optical power to generate photocurrent, equal to the rms noise current in a 1 hertz bandwidth. The NEP is roughly the minimum detectable input power of a photodiode

## Slide 43: Other Photodetectors
The detectors used in fibre–optic are more complex than simple photodiodes.
PIN (p-intrinsic-n) Diode
Device with an intrinsic layer between p and n type layers is called PIN diode.
As the absorption of light increases with the thickness of depleted region. A pin photodiode come pre-depleted, the intrinsic region lacks the impurities needed to generate current carriers in the dark.
By concentrating absorption in the intrinsic region, it avoids the noise and slow response that occurs when the p region of ordinary pn photodiode absorbs some light.
Avalanche Photo-diodes
In these photodiodes when reverse bias voltage is increased sufficiently, an avalanche effect occurs and the optically generated current can be amplified

## Slide 44: Applications
Photodiodes are used in similar applications to other photo detectors, such as photoconductors, charge-coupled devices, and photomultiplier tubes.
Photodiodes are used in consumer electronics devices such as compact disc players, smoke detectors, and the receivers for remote controls in VCRs and televisions.
Photodiodes are often used for accurate measurement of light intensity in science and industry. They generally have a better, more linear response than photoconductors.
PIN diodes are much faster and more sensitive than ordinary p-n junction diodes, and hence are often used for optical communications and in lighting regulation

## Slide 45: Thank You