## Slide 1
Advanced Manufacturing and Integrated Photonics Certificate Program (AMIP)
Developed by Stonehill College and Bridgewater State University, in cooperation with the Initiative for Knowledge and Innovation in Manufacturing at MIT, with funding from the Office of Naval Research (grant # N00014-18-1-2890)
All materials may be freely used, reproduced, and adapted, provided that credit is properly attributed to the AMIP consortium and to the specific author of this course module.
Course module: Tools and Testing Equipment
Topic 3
Topic title: Circuits, troubleshooting, & soldering
Author: Bruno Nosiglia/David Simon

## Slide 2: Brief Introduction to optical measuring devices

## Slide 3: Light is a wave
Light is an oscillating set of electric and magnetic fields.
Both the electric and magnetic fields have the same period, so it suffices to look just at the electric field.
The speed of light is 186,282 miles per second
The frequencies are typically around 1014 oscillations per second, and the wavelengths are around a tenth of a micro-meter.
Electric field
The light wave travels this way
The color of the light is determined by the frequency (or equivalently, by the period or wavelength)

## Slide 4: Optical measurement
Since light is easy to produce and measure, it is ideal for many types of optical measurements.
Besides producing images (pictures of an object), light can be used to measure an array of quantities, including:
  Distances between objects
  Times between events
  Speeds of objects (using the Doppler effect)
  The energy difference between two states of an atom

## Slide 5: Optical measurement
In addition, properties of the light itself can be measured.
These properties include:
  Period, wavelength, frequency
  Direction that the electric field points (polarization direction)
  The phase shift between two beams of light.
Phase shift is a measure of how much one beam is displaced relative to the other:
The distance between the crests gives a measure of the phase shift. Phase measurements can be used determine other quantities such as the sizes of very small objects.

## Slide 6: Optical Instruments
A variety of optical instruments have been developed in order to either:
  Measure the properties of the light itself
  To use the light to measure other things.
In general, light with smaller wavelengths and higher frequencies can provide measurements with higher resolution (ability to measure smaller details).
In the following slides, a brief introduction is given to several optical instruments.
Some of these instruments will be discussed in more detail in later courses in this program.

## Slide 7: Microscope
The best-known optical instrument is the microscope.
It produces magnified images of small objects.
The magnification is determined by the focal lengths (a measure of the bending power) of the lenses used.
The resolution is determined by the wavelength of the light and the diameter of the lenses. (Better resolution requires shorter wavelengths or larger-diameter lenses).
Schematic of simple microscope:

## Slide 8: Interferometer
When two light beams are combined, they interfere, meaning that they produce a series of light and dark bands.
At some point constructive interference occurs: the crests of the two waves are on top of each other, so the total beam is the sum of the two. The result is a bright spot.
At other points destructive interference occurs: the crest of one wave coincides with the trough of the other, so the total beam is the difference of the two. The result is a dark spot spot.
From the distance between two adjacent bright spots, the phase difference between the beams can be determined.

## Slide 9: Interferometer
There are many types of interferometers. One very simple type is shown schematically below:
Incoming beam 1
Incoming beam 2
Outgoing beams
The cube shown at right is a beam splitter: a type of mirror that reflects part of each beam and transmits part.
The two outgoing beams are mixtures of the two incoming beams.
When the outgoing beams are reach a screen or a camera, they produce an interference pattern.

## Slide 10: Autocollimators
An autocollimator is a device for measuring deviations in the angles of different light rays.
By tracing these rays backward, they can detect changes in the surface of an object off of which that light has reflected. The degree of flatness of the surface can be measured.
Applications include:
  Quality control of manufactured parts: are the surfaces smooth?
  Are two beams in an optical setup properly aligned with each other?
  Are there imperfections in a silicon wafer from which integrated electronic chips will be made?

## Slide 11: Optical profilometer
A profilometer measures the shape or profile of a surface.
Optical profilometers generally use interferometry of some kind: a beam reflected from the surface is made to interfere with a reference beam.
Profilometers are often used in quality control to measure the surface of a milled part or an integrated chip.
Profilometers often make use of scanning: a small area of the surface is probed at each moment, and the probe is then moved sequentially to cover the entire surface, forming a picture one pixel at a time.
The probe is often an optical fiber.

## Slide 12: Optical time-domain reflectometer
An optical time-domain reflectometer is used to characterize the properties of an optical fiber.
A series of optical pulses are sent along the fiber, and the amount of light reflected back to the input end of the fiber is measured.
The amount of light reflected back is a measure of imperfections in the fiber.
The time delay between the incident and reflected pulse gives a measure of the location of the imperfection along the fiber.

## Slide 13: Spectrometer
A spectrometer measures the frequencies in a beam of light. The range of frequencies is called the spectrum.
There are two main ways to measure the spectrum:
  Through bending of the light: prisms and other devices will bend different frequencies by different amounts. The result is a rainbow, with different colors (frequencies) separated from each other.
  By diffraction: the light is sent through a grating. The parts of the beam that passed through different parts of the grating will interfere with each other. The wavelength can then be found from the interference pattern.