## Slide 1
Advanced Manufacturing and Integrated Photonics Certificate Program (AMIP)
Developed by Stonehill College and Bridgewater State University, in cooperation with the Initiative for Knowledge and Innovation in Manufacturing at MIT, with funding from the Office of Naval Research (grant # N00014-18-1-2890)
All materials may be freely used, reproduced, and adapted, provided that credit is properly attributed to the AMIP consortium and to the specific author of this course module.
Course module: Tools and Testing Equipment
Topic 1
Topic title: Overview, Safety, & Measurement Basics
Author: Bruno Nosiglia

## Slide 2: Safely using measuring tools in a photonics lab
Photonics = a name that comes from photons (light) – the study and use of light in technology
OSHA = a section of the federal government that protects workers and teaches them safety
Tool = a device used to perform a specific task to build or repair
Instrument = a device used to measure, requires more skill
Metric system = a system of measuring that is based on 10
English/Standard/Imperial system = system of measuring that is based on old inches, feet, pounds, miles, etc.

## Slide 3: Calipers

## Slide 4: Watch video, on how to use a caliper - https://www.google.com/search?rlz=1C1GIGM_enUS674US674&ei=tulvXtC6NsWlytMP_LaFqAk&q=how+to+use+a+caliper&oq=how+to+use+a+caliper&gs_l=psy-ab.1.0.0l10.324958.326516..328268...0.3..0.111.548.6j1......0....1..gws-wiz.......0i71j0i67j0i10.9KuEfr-UHOw#kpvalbx=_AOtvXu65BqKOggeUkaWgBA35
Calipers – used to measure diameter of holes, depth of holes, & outside dimensions
Calipers points are placed over or in an item to be measured, the dial is turned until it just touches the item. The dimesion measurement is read off the dial or display
Calipers are used for larger items, for very small or thin items,micrometers are used.

## Slide 5: Micrometer

## Slide 6: Watch video, on how to use a Micrometer - https://www.google.com/search?q=how+to+use+a+micrometer&rlz=1C1GIGM_enUS674US674&oq=how+to+use+a+micrometer&aqs=chrome..69i57j0l7.8383j0j8&sourceid=chrome&ie=UTF-8#kpvalbx=_tulvXtC6NsWlytMP_LaFqAk78
Micrometer – used to measure thicknesses of very thin or very small items
Micrometer anvils are placed over an item to be measured, the dial is turned until it just touches the item. The dimension measurement is read off the dial or display
Micrometer is so sensitive that even the thickness of dust can be measured, so this instrument must be kept perfectly clean.

## Slide 7: Reading a measuring system

## Slide 8: Mechanical drawing

## Slide 9
Tolerance = the amount of error a customer will tolerate before it is rejected
Precision = how exact a measurement is, how many decimal places it is measured to